SECTION 1.E.0 - SUPPLEMENTAL SPECIAL CONDITIONS

- GENERAL INFORMATION

A.	PROPOSAL OUTLINE

1.	Description

The Curators of the University of Missouri invite proposals for the design and construction of the  VIRGINIA AVENUE PARKING STRUCTURE  at the University of Missouri - Columbia, Columbia, Missouri.

The Scope of the Project is to design and construct a multi-level parking structure with associated site and utility work between Hitt Street and Virginia Avenue just north of the Ambulatory Care Facility.

The Proposer shall furnish all Architectural and Engineering services for development of the design and preparation of working drawings and detailed specifications to complete the project; including civil, structural, mechanical and electrical engineering in accordance with the requirements of the Contract Documents.  The Proposer shall use one entity of the design team as the Prime Professional.

From the working drawings and detailed specifications approved by the Owner, the Proposer shall furnish all labor, materials, equipment, services and transportation necessary to complete construction of the parking structure.

The work of the Contract shall be restricted to that area indicated on the Design/Build Guidelines Drawings as the ALimit of Work.@  No material, equipment or debris shall be deposited upon any area outside of the ALimit of Work@ unless prior approval has been obtained from the Owner= Representative.

2.	Design/Build Procedure

The procedure being utilized for this contract is commonly referred to as the Design/Build Method.  Prospective Proposers should carefully examine all Requests For Proposal (RFP) Documents, Design/Build Guidelines and the site prior to submitting a proposal on this project.

Each Proposer (Design/Builder) will be required to use licensed Architects and Engineers, registered with the State of Missouri, to prepare the designs and assure that all work and professional services are being performed as expertly as possible. The Design/Builder=s Architect or Engineer shall serve as the Prime Professional.

All drawings, specifications and calculations prepared by the Architects and Engineers secured by the Design/Builder shall be sealed by State of Missouri Registered Professionals and shall adhere to all requirements of the AConsultant Procedures and Design Guidelines@ of the University of Missouri which are held by many consultants throughout the State.  For those not holding current volume (April 1998 with September 1998 addenda), contact Facilities Planning & Development, 6 Clark Hall, Columbia, Missouri 65211, (573) 882-2321.  A $50 refundable deposit is required.  The successful design/build team will receive the AConsultant Procedures and Design Guidelines@ at no charge for use on the project.  Where the RFP Documents and Guidelines Specifications establish requirements more stringent than the AConsultant Procedures and Design Guidelines,@ the RFP Documents and Guidelines Specifications shall govern.

Work in the public R.O.W. require permits to be secured by this contractor, and all work shall conform to the specification of the City of Columbia, Missouri.  Where work is indicated to comply with City of Columbia standards and the RFP Technical Specifications establish requirements more stringent than the City of Columbia standards, the RFP Technical Specifications (including the AConsultant Procedures and Design Guidelines@) shall govern.

Each proposer is required to submit a technical proposal that would produce the best overall project for the intended purpose within the not-to-exceed project budget shown in SSC paragraph I.A.3.  This technical proposal shall be an integral part of each proposal and, when reviewed and evaluated in accordance with Evaluation Procedures, SSC Section III, shall be used in the determination of the best proposal.

The intent of the Design/Build Guidelines is to establish design objectives and minimum acceptable construction standards.  The Owner encourages the use of creative and innovative design solutions in meeting program requirements and fulfilling the intent of the Design/Build Guidelines.  The Owner is interested in innovations that will result in the Owner realizing greater value in the constructed project.  The Owner reserves the right to determine whether proposed creative and innovative solutions fulfill the intent of the Design/Build Guidelines.

AProgram and Design Criteria@ (see Supplemental Special Conditions, Section II) sets forth in detail the conditions and limitations of the property to be utilized for construction of this project and the Program Design Requirements.

Design/Build Guidelines Sections in Divisions 2 through 16 specifies the minimum standards of construction acceptable to the Owner.  These standards are established by reference to standards commonly used in the Construction Industry except where otherwise noted.

The Owner=s evaluation board, comprised of University of Missouri System and University of Missouri - Columbia professional staff, administrators, faculty and student representatives, at its discretion, may give consideration to proposed creative and innovative methods, which may not exactly match criteria listed in the Design/Build Guidelines, yet fulfill the intent of the design objectives and meet the minimum standards of the Design/Build Guidelines.  The Owner reserves the right to determine whether proposed creative and innovative methods fulfill the intent of the Design/Build Guidelines.

3.	Design/Build Budget and Time Limit

The project must be completed and ready for occupancy within SIX HUNDRED TWENTY (620) calendar days from receipt of contract.

Design and construction fund budgeted for the Project is $ 13,500,000.  Proposals that exceed this budget shall be rejected.

B.	QUALIFICATION FOR PROPOSAL

- The prospective Proposer must be a bonafide company having constructed at least 3 parking structures and have five (5) years experience constructing the type and the approximate size of the work indicated in these proposal guidelines and available for inspection by designated personnel of the Owner.

2.	The prospective Proposer must be able to prove ability and experience of their Prime Professional=s team to design the type and size facilities indicated in these Design/Build Guidelines and show past experience that the Prime Professional=s team has in working with the Proposer.

3.	Proposals submitted that do not demonstrate adequate experience may be considered non-responsive and are subject to rejection.

II.	PROGRAM AND DESIGN CRITERIA

A.	PARKING STRUCTURE SITE DESIGN

1.	Site Design

1.1	The Site is generally bounded by Virginia Avenue on the east, University property on the south, Hitt Street on the west and University property and one privately owned parcel on the north.  The site slopes approximately 20 feet from the north to the south.

1.2	The Project includes addition of a traffic lane on Virginia Avenue in accordance with the City of Columbia specifications.

1.3	The project includes the removal of existing site utilities (including electric lines, water lines, storm water lines, etc.) to accommodate the new parking structure and street reconstruction, and the construction of new utilities including underground electric from MU system, water from MU system, telephone from MU system and sanitary and storm sewers from City of Columbia.

1.4	The Owner will Design and install the Project landscaping under a separate contract.  Consideration should be given in the design to the provision of open areas around the parking structure where landscaping can be used to soften the structure and to provide transition between the parking structure and adjacent buildings.  The Contractor shall rough grade all areas to receive grass or plant material six (6) inches below finish grade.

2.	Site Planning Factors

2.1	The structure is located on prime University land and dictates a relatively high density of use.  The use of the maximum site area to accommodate the parking structure will serve to minimize the parking structure height and attain this density.

Refer to Site Dimension Plan for >build to= lines on north and west sides of the parking structure and minimum set-backs on south and east sides of the parking structure.

2.2	Refer to the Topographic Survey prepared by  ENGINEERING SURVEYS & SERVICES  for complete site utility information.  Locations of utilities shown are approximate; it is the responsibility of the Design/Builder to determine exact locations.

2.3	Provide for safe removal and disposal of any hazardous or toxic materials or substances identified in the Environmental Site Assessments, as shown in the Asbestos Survey Report, in accordance with the applicable regulations of the U.S.E.P.A., Missouri Department of Natural resources and any other governing agencies

2.4.	Meet any and all Federal, State and Local regulations regarding storm water runoff and erosion control during construction.

2.5	Vehicular Access

The grade drop across the project site should permit on grade access to the two lower levels of the parking structure.  A combined entrance/exit shall have a minimum width of 25'-0" (two (2) 12'-6" drives).  A separate entrance/exit shall have a minimum width of 13'-0".  Separate entrance/exits may not be separated by more than 100'-0" horizontally.

2.6	Pedestrian Access

Predominate pedestrian paths to and from the parking structure will be from the northeast and northwest.

A major access point which will include a stairway and elevator serving floors two (2) thru six (6) shall be located in the northwest corner of the parking structure.

Pedestrian accessible routes to the parking structure at each stairtower and stair/elevator  location, meeting ADAAG requirements shall be provided.  Note - accessible route will not be required to east, center stairtower.

Where pedestrian traffic encounters curbs, the curb edges shall be clearly marked with paint.

2.7	Sidewalks

All sidewalks and curb cuts shall conform to the widths shown on the Drawings, the Consultant Procedures and Design Guidelines and ADA.

2.8	Site Furnishings

Provide bike racks at the northwest stairtower and at the Campus Police entry on the southeast corner of the parking structure.  One 16' unit and one 20' unit.

2.9	Site Lighting

Provide conduit and bases per the Consultant Procedures and Design Guidelines.

3.	Civil Engineering

Design and calculations shall be prepared by a Civil Engineer licensed in the State of Missouri and shall conform with the codes and standards referenced in Special Conditions, Article 10 and the City of Columbia.

3.1	This project includes site development in the form of the reconstruction of a portion of Virginia Avenue and utility installation.  The requirements for the construction of these improvements is tightly controlled by both the City of Columbia and the University.  Final design should include storm water calculations in accordance with the University of Missouri design criteria.

3.2	All work on public utilities must conform to that utility=s requirements.  All work on the  addition of the lane on Virginia Avenue must conform to the City of Columbia standards.  All work on University utilities must conform to University standards.  Where City of Columbia standards are less stringent than University standards, University standards will govern.

3.3	All street and utility work must conform to the phasing and access requirements outlined herein.  Utilities to buildings not owned by the University must be coordinated with the utility company to provide the minimum amount of time that the building will be without service.

The successful Proposer will be required to design, submit and implement a traffic control plan approved by the Owner and the City of Columbia.

3.4	The minimal scope of work with respect to electrical duct banks and water mains shall be defined as that required to meet the following criteria:

- The proposed solution must meet the requirements outlined elsewhere in these documents for continuity of service to the University.

- The proposed solution must provide the new University water main sizes indicated elsewhere in the documents.

- The proposed solution must provide the upgraded high-voltage electrical cabling and conduits indicated elsewhere in the documents.

B.	PARKING STRUCTURE DESIGN

1.	Qualifications and Standards

1.1	Structural Design and calculations shall be prepared by a Structural Engineer licensed in the State of Missouri and shall conform with the codes and standards referenced in Special Conditions Article 11 and other standards that may not be listed but are commonly used as standards for design of this type project.

2.	Parking Structure

2.1	Parking Structure Structural Systems:

There are three acceptable types of structural systems for this Project.  The systems are as follows:

- Cast-in-place post-tensioned concrete frame and deck.  Refer to Technical Specification Section 03300 for cast-in-place concrete requirements and Section 03311 for post-tensioning systems requirements.  Exterior spandrel panels and columns may be architectural cast-in-place concrete, architectural pre-cast concrete/plant cast.  Brick or stone masonry may be inset into the panels.  Structure will have a traffic topping membrane at all construction joints.  Post-tensioning tendons and anchors shall be encapsulated.  All elevated concrete slabs and beams shall have epoxy coated bars (except beam bottom steel) and/or epoxy coated mesh and shall have silica fume admixture.

- Pre-cast prestressed concrete double tee slabs with pre-cast concrete frames and shear walls and a cast-in-place topping slab.  Refer to Technical Specification 03350 for concrete toppings and Section 03410 for structural pre-cast concrete/plant cast.  Exterior spandrel panels and columns may be architectural pre-cast/plant cast.  Brick masonry may be inset into the panels.  Structure will have polyethylene fibers in topping slab.  All structural connections utilizing coil rods and embed plates shall be coated with galvanizing repair paint.  All weld hardware shall be placed at least 3/4" from the surface.  Concrete topping shall have epoxy coated mesh.  All elevated concrete slabs and beams shall have epoxy coated bars (except beam bottom steel) and/or mesh.

- Pre-cast prestressed concrete pre-topped double tee slabs with pre-cast concrete frames and shear walls.  Refer to Technical Specification Section 03410 for structural pre-cast concrete/plant cast.  Exterior spandrel panels and columns may be architectural pre-cast concrete/plant cast.  Brick or stone masonry may be inset into the panels.  All structural connections utilizing coil rods and embed plates shall have these components galvanized.  All welding of this material shall be coated with galvanizing repair paint.  All weld hardware shall be placed at least 3/4" from the surface.  All slab flanges shall have epoxy coated bars or mesh.  All elevated concrete slabs and beams shall have epoxy coated bars (except beam bottom steel) and/or mesh.

- All three structural systems will have galvanized slab embeds, a sloped wash around columns and at slab perimeter, and sealed joints at full depth cracks.

- With all three structural systems, the use of a structural steel frame is permitted for only the exit stair and roof framing.

- Combinations of the three structural systems are acceptable.

2.2	Foundation Design:

The foundation system shall be designed by the Proposer.  Subsurface Investigation, Soil Analysis and Foundation Design Recommendations for the Virginia Avenue  Parking Structure at MU and supplemental letter dated August 1, 2000, as 	prepared by Engineering Surveys and Services is included within the Design/Build Guidelines, Appendix A for the Proposer=s information only.  Refer to Guidelines Specifications 02200 and 02380 for the Proposer=s responsibility with respect to foundation design.

2.3	Structural Planning Considerations:

- The parking structure should provide for the greatest extent of clear span parking possible.  Vertical elements should be as transparent as feasible to create visual and psychological openness in the parking areas.  Vertical elements may not intrude into the width or depth of clear parking stall dimensions, except intrusions of not more than 1=-0@ deep and 1=-0@ wide may occur at the front corners of stalls adjacent to striping between stalls.  Long vertical elements, such as shear walls or stair enclosures, should be planned to provide sufficient clear sight lines.

B)	The parking structure shall allow for minimum clear heights in aisles and in parking stalls as follows:

Street Level (First and Second Levels) = 10'-6@ clear minimum (van accessible)

Other levels = 7=-6@ clear

These clear heights shall be as measured below all horizontal projections, including light fixtures, signs, piping and electrical conduits that will interfere with parking and internal vehicular and pedestrian circulation. Elements projecting below clearance lines that do not extend more than 2= below required clearance, will be allowed at front of parking stalls if located horizontally within 2= of columns or wall face.  Any items that are permitted to project into the clearance envelope shall be placed as high and as close to column or wall face as possible.

C)	Ramp systems containing parking stalls shall not exceed a slope of 5.5%.

D)	All grade and elevated slabs, shall be sloped to drain. The minimum slope perpendicular to drive lanes shall be 2% and the minimum slope parallel to drive lanes shall be 1-1/2%.  Camber in the structure and short and long-term deflections shall be controlled by design to maintain these drainage requirements.  All resulting valleys shall have sufficient slope so they will not pond water.

E)	Provide an 8@ minimum clear vertical chase between ramps for vertical pipe and conduit runs.

F)	If expansion joints are placed in the structure, the joint shall occur on each elevated parking level and independent support shall be provided on each side of the joint.  If the structural system is cast-in-place concrete, separate columns and beams shall be located on each side of the joint.  If the structural system is precast concrete, stems of adjacent double Ts shall be located on each side of the joint so there are no overhanging flanges.  Beams supporting double Ts shall be supported by separate columns on each side of the joint.  Joints shall pass completely through exterior finishes.

- Visual/Aesthetic Factors

3.1	Architectural Design shall be prepared by an Architect licensed in the State of Missouri and shall conform with the codes and standards referenced in Special Conditions Article 10 and other standards that may not be listed but are commonly used as standards for design of this type project.

3.2	The University of Missouri - Columbia desires the structure to reflect the  college Gothic theme set by the older Awhite campus@ buildings: Cramer, Defoe, Rothwell, Brewer, McKee, Read, Gentry, Memorial Student Union, Whitten, Mumford, Waters, Lefevre, Stephens, Schweitzer, Schlundt, Schlundt Annex, Curtis, Stewart and Gwynn.

The specific architectural treatment shown on the Design/ Build Guidelines drawings is intended to convey a general sense of desired character and use of texture; it is in no way intended to limit the Proposer=s use of innovative and creative design solutions.  In keeping with that goal, the following criteria shall be followed:

D)	Floor levels of the parking structure are to be expressed on the exterior as level; expression of sloping floors or ramps is not acceptable on any side.

E)	The aesthetic theme shall be complimentary to the Awhite campus@ college Gothic using exterior cladding color of white or near-white buff material.

F)	The exterior cladding shall be brick or stone masonry, architectural precast concrete or cast-in place concrete of matrix approved by the University and have features to provide the following:

- Expression of the vertical columns; vertical expression is recommended as appropriate for the college Gothic theme.  Relentless horizontal expression is not appropriate for the college Gothic theme.

- The architectural palette may include Gothic features such as a regular vertical rhythm; Gothic arches; significant relief features at entrances; and other features appropriate to the design theme.

D)	Finishes:

1)	 The amount of masonry shall be similar to that shown on the Design/Build Guidelines Drawings.

2)	Durable finish, factory painted aluminum shall be used to frame glazed areas.

- Precast exterior finishes, if used, shall enrich the architectural character and college Gothic theme of the design by the use of a combination of finishes which may include:

- Exposed aggregate by chemical retarders or water washing.

- Form liners.

- Sand or abrasive blasting.

- Tooling or bush hammering.

- Honed or polished.

- Stone veneer-faced panels (match stone of existing Awhite campus@).

- Cast in place exterior finishes, if used, shall enrich the architectural characer and college Gothic theme of the design by the use of a combination of finishes which may include:

- Use of white portland cement in combination with special concrete finishes.

- Exposed aggregate by chemical retarders.

- Form liners.

- Sand or abrasive blasting.

- Tooling or bush hammering.

- Hammered rib or fractured fin.

Combinations of different finishes within a single precast or cast in place unit offer excellent possibilities for the architectural use of tones and texture in the facade treatment and are encouraged.

E)	The major mass of parking structure shall have a height that represents a SIX STORY building above the level of the existing grades at the south end of the site.

F)	Mockup Requirements:

Mockup panels, representative of all exterior sections, showing all exterior materials and finishes shall be required prior to construction for approval of finishes by the University.

4.	Light/Air Quality/Security/ Factors

4.1	Light Control:

The exterior enclosure should control any vehicular headlamp glare escaping the parking structure and impacting neighboring facilities.

4.2	Air Quality:

The structure should be naturally ventilated in accordance with the referenced building codes to obtain an AOpen Parking Structure@ classification.  Natural ventilation should utilize prevailing winds and open sidewalls, areaways, and/or site grading to avoid any stagnant areas where fumes would accumulate.

4.3	Security:

The structure should provide an optimum level of safety and security for users at all times.  Structures that create dark and confined spaces must be avoided.  Maximum visibility of stairs and elevators from inside and outside the structure is desirable.

Glass protecting stair and elevator shafts from weather elements shall be tinted to allow high degrees of visibility day and night.  Areas below stairs and ramps must be enclosed with concrete or concrete masonry units.

Guards along interior slab edges at sloping ramps, except at the roof level, and on each side of ramps between tiers, shall be of an open design that provides minimal visual restriction while complying with code requirements.  Guards along interior slab edges at the roof level shall be concrete.

4.4	Snow Dumps:

The structure should provide a minimum of four (4) snow dump locations, one per side, for the Owner=s maintenance personnel to safety dump snow over the top deck parapet.  Design shall protect pedestrians, moving vehicles and parked vehicles from dumped snow and prevent dumped snow from blowing into the parking garage.

5.	Traffic/Parking Planning Elements

5.1	Internal Circulation:

The parking structure shall generally utilize one-way circulation with angled parking; exceptions are that two-way circulation is permitted on cross aisles and entrances.  The general operation of the structure will be for use by self-parkers without assigned or reserved spaces.  Internal circulation should serve to minimize cross-traffic or traffic conflict points, should allow for minimal Asearch@ / Aexit@ time and should allow for ease of vehicular re-circulation to facilitate traffic flow.  Dead ends should be avoided and in no cases should there be more than one dead end in the garage.

5.2	The Design/Builder is restricted to the general configuration of the FOUR BAY parking structures and the locations of the entrance and exit shown on the Design/Build Guidelines Drawings. The Design/Builder may use alternative parking stall angle schemes that will achieve the requirements in the Design/Build Guidelines and produce the greatest number of parking spaces at the least cost.

5.3	The design must address pedestrian and vehicular patterns.

5.4	Stall Design:

Parking stall design angle shall be between 50o and 70o (increments of 5o); 90o stalls shall only be used where they are located at end of a driving lane providing straight-on entry; and shall be in alignment with a one-way traffic flow.  Parking stall and drive lane dimensions shall afford a high degree of comfort/service.  All parking stall shall be based upon large cars with no reduction or weighted averaging for compact cars.  Compact car stalls will not be considered.  Minimum dimensions for parking stalls and traffic lanes are as follows (width is center to center):

Standard Spaces

Stall width - (50E - 65E angle stall width = 8'-4"; 70E and 90E stall width = 8'-6@)

Stall length - 18'-0" (painted stall line length) clear of all obstructions

50E Stalls

Vehicle Projection				= 18'-8"

Aisle Width					= 15'-0" one way

Aisle Width					= 20'-0" two way

Interlock Reduction			= 2'-1"

Parking Module/Wall to Wall		= 52'-4"

Parking Module/Wall to Interlock	= 50'-3"

Parking Module/Interlock to Interlock	= 48'-2"

55E Stalls

Vehicle Projection				= 19'-2"

Aisle Width					= 16'-0" one way

Aisle Width					= 20'-0" two way

Interlock Reduction			= 1'-10"

Parking Module/Wall to Wall		= 54'-4"

Parking Module/Wall to Interlock	= 52'-6"

Parking Module/Interlock to Interlock	= 50'-8"

60E Stalls

Vehicle Projection				= 19'-6"

Aisle Width					= 16'-0" one way

Aisle Width					= 20'-0" two way

Interlock Reduction			= 1'-8"

Parking Module/Wall to Wall		= 55'-0"

Parking Module/Wall to Interlock	= 53'-4"

Parking Module/Interlock to Interlock	= 51'-8"

65E Stalls

Vehicle Projection				= 19'-8"

Aisle Width					= 17'-0" one way

Aisle Width					= 20'-0" two way

Interlock Reduction			= 1'-4'

Parking Module/Wall to Wall		= 56'-6"

Parking Module/Wall to Interlock	= 55'-2"

Parking Module/Interlock to Interlock	= 53'-10"

70E Stalls

Vehicle Projection				= 19'-10"

Aisle Width					= 18'-0" one way

Aisle Width					= 20'-0" two way

Interlock Reduction			= 1'-1"

Parking Module/Wall to Wall		= 57'-8"

Parking Module/Wall to Interlock	= 56'-7"

Parking Module/Interlock to Interlock	= 55'-6"

Buried stalls are not allowed.  Where stalls abut vertical elements with a horizontal 			dimension parallel to the length of the stall in excess of 2'-0", the overall stall width shall be increased from 8'-4" to 9'-6.@

Universal accessible parking spaces, conforming with ADA, shall be provided.  A 3-foot covered accessible route shall be provided in front of the accessible spaces, and lead to the elevator.  Spaces shall be distributed on Levels One and Two as indicated on the Design/Build Guidelines.  All accessible spaces shall be on perimeter of garage.

5.5	Entry/Exit:

At points of entry/exit, visual obstructions should be minimized to avoid unobstructed visibility of all vehicular and pedestrian traffic.  Roadway design will be based upon 25  MPH on wet pavement.

5.6	Graphics/Signage

A)	General:

Provide sufficient graphics so as to direct and identify the most convenient means of vehicular and pedestrian access.  Graphics should be simple, easy to read and clearly visible.  Interior signage design shall be in accordance with referenced codes and standards.  There are no campus graphic standards for interior signage.  Provide AClearance Bars@ at entry, exit and within parking structure at changes in clear heights on Street Level indicating change in clear heights.  All signage mounted on ground or parking structure to identify garage name, entrance and exit shall be provided and installed to meet University standards.

B) 	Design Criteria:

Provide the following minimum signage:

A	At the end of each aisle or ramp - direction to more parking

A	At the end of each aisle or ramp - direction to exit

A	At each level Bdirection to elevator and/or stairs

A	At each level at each stair B level or tier designation - indicate roof access

A	As needed - direction to pedestrian exits

A	At Street Level and as needed on other levels - direction to accessible stalls

A	As needed - direction to accessible spaces

A	As needed - direction to emergency phones

A	At street Level on grade to designate entrance and exit

A	At entrance and exit to designate clearances in the parking structure for standard and van accessible vehicles

A	In interior of structure to designate changes in clearances

- Provide international symbols on all signs where appropriate

- Traffic directional signs should be placed in the center of the drive aisles (ceiling mounted)

6.	Vertical Circulation/Shell Office Space

6.1	Passenger Elevator:

Provide a 3500-pound capacity glass-backed hydraulic passenger elevator at the northwest corner of the parking structure.  Elevator cab size shall meet the requirements of ADA.  Elevator is to serve parking levels as shown on the drawings. If curbs are provided at elevator landing ADA-accessible curb cuts shall be provided.

Interior finishes of elevator cab, doors, and frames are to be stainless steel.  All elevator controls and indicators shall use a vandalism-resistant design.  Use stainless steel call buttons with central light-up jewel.  Other signal fixtures in cab and hall, including car direction lantern and car position indicator shall be of similar vandal resistant design.

6.2	Exit Stairs:

A minimum of four stairs shall be provided at locations shown to accommodate major pedestrian ingress/egress points.  Stairs shall have a minimum width of 5'-0" and shall have open railings to maintain visibility.  Stair landings should be separated by sloping floor complying with ADA accessible route requirements.  Curb cuts must be provided at all stairs directly accessing the exterior.

Exterior walls of exit stair/elevator towers shall be glazed at a minimum 50% of the exterior wall area.  Exterior doors are not required at grade, with the exception of the elevator tower.  Exit stairs at the roof top parking level shall be fully enclosed and finished on all sides to match the theme of the building.  Exit stairs may be open to the parking area, with the exception of the exit stair/elevator combination, which should share a common enclosed lobby.  Enclosed Elevator Lobby, at parking structures levels one and two, shall have doors equipped with power door operators.

Stairs at tiers below the roof shall be open to the parking area.

Non-glazed stair wall finishes shall include either smooth precast finished, smooth-formed rubbed cast-in-place concrete, concrete masonry units or a combination of these types with painted finish.  Stair finishes shall include painted concrete or concrete masonry units, painted stair pans and painted metal railings.  Stair construction can be concrete or concrete filled steel pans.

6.3	Shell Office Space:

Provide a minimum of 14,000 gross square feet of shell office space for MU Campus Police and a minimum of 7,500 gross square feel of shell space for Landscape Services within the first level of the structure, with the area having a minimum of 10'-6" clear from finish floor to underside of any structural element.  Utility and service rooms shall be a part of this shell space requirement.

Shell office space shall be separated from the parking area by a concrete masonry unit partition.  A vestibule with power operated pairs of doors shall be at the main entry for MU Campus Police with three additional exit doors, two into the garage and one to the exterior.  The shell space shall include all exterior windows and interior and exterior doors.  Amount of glazing shall be proportional to what is shown on drawing sheet A200.  Two overhead doors, a single main entry door to the exterior and a single door into the parking structure will be provided for Landscape Services.  The slab above the shell space shall receive a watertight membrane between the structural slab and a poured-in-place top slab.  If precast structural system is used, a span not to exceed 31'-0" shall be used over the shell space.  The underslab gravel, but no slab-on-grade, is required within the shell spaces except as noted for the mechanical/electrical room in the MU Campus Police space.  6" recess to top of gravel.

6.4	Specialties:

A)	Security Screening: Provide black vinyl coated chain link security screening at all garage openings which are within 10'-0" of finish grade.

B)	Trash Receptacles: Provide trash receptacles at the exit stair on each floor level.

C)	Phone Enclosures: Provide windbreak phone enclosures at rooftop emergency telephones.

D)	Bicylce Parking: Provide bicycle parking racks at both the northwest and southeast entrances.

7.0	Mechanical Design:

Mechanical Design and calculations shall be prepared by a Mechanical Engineer licensed in the State of Missouri and shall conform with the codes and standards referenced in Special Conditions Article 10 and other standards that may not be listed but are commonly used as standards for design of this type project.

7.1	Mechanical Systems

Parking areas are to be naturally ventilated.

7.2	Equipment Rooms HVAC

Provide a packaged heating, air conditioning and ventilating unit to condition the elevator equipment room.  Collect condensate from AC unit and pipe to drain. Ventilation shall be provided per ASHRAE requirements and provide heating and cooling capacity to meet environment requirements of elevator manufacture. Provide positive powered ventilation of elevator shaft to control heat buildup.

Provide forced air ventilation as required for electrical equipment room.

7.3	Plumbing Systems

Provide a Water Service Room sized according to referenced codes and standards.  Provide a floor drain in this room and a locking entrance door accessed from the garage area.

Provide water service valved and capped in the water service entry room for perimeter water hydrants and wash down water systems.

Provide exterior freeze proof yard hydrants for landscape maintenance at grade no less than 150'-0" on center on the perimeter of the parking structure. Mechanical Room shall have floor drain.  Tie all shell area drains into the site sanitary sewer service.

Provide floor drains throughout the parking area to drain the structure.  Locate all exposed vertical piping within parking areas and in the open vertical chase provided between parking ramps adjacent to columns or vertical structural element.  Provide trench drain at base of highest ramp.  Trench drain shall be full width of ramp.

7.4	Fire Protection Systems

Provide a fire protection system as required by Guidelines Specification Section 15375.  A system of Class I dry standpipes with 2-1/2 inch hose valves and 1-1/2" reducers at each level visible from stair landings and siamese connections shall be designed and installed per NFPA-14 and BOCA standards.  Siamese connections shall be type as and located per local fire department requirements.  Locate all exposed vertical piping within parking areas in chase and horizontally positioned near vertical structural elements.  Where pipe or hose valves can not be in the chase they shall be located between parking stalls.

8.	Electrical Systems:

8.1	Electrical Design:

Electrical Design and calculations shall be prepared by an Electrical Engineer licensed in the State of Missouri and shall conform with the codes and standards referenced in Special Conditions Article 10 and other standards that may not be listed that are commonly used for design of this type project.

8.2	Electrical Service:

The electrical service shall be fed from a pad mounted transformer, provided by the Contractor.  The main service entrance to consist of a 480Y/277V, three phase, four wire, main circuit breaker panelboard located in the Electrical Equipment Room on the lowest level of the parking structure. The service entrance panelboard shall be grounded in accordance with the NEC. The main service panelboard will serve 277V lighting loads and 480V three phase equipment loads. Provide a solid state, 1.0% accuracy class meter with digital read out per the specifications of the following metered values:

A)	Demand (kW-H)

B)	Apparent Power (kVA)

C)	Reactive Power (kVAR)

D)	Current (A)

E)	Voltage (V)

F)	Power Factor (PF)

Receptacle and small power panels will be 208Y/120V, three phase, four wire, fed through a 480-208Y/120V three phase, dry-type transformer.

8.3	Emergency Power:

Emergency power for Code required egress lighting, exit lighting and emergency systems shall be provided by a central battery/inverter system located in the Electrical Equipment Room.

8.4	Lighting:

The lighting design for parking, driveway and stairs will utilize cutoff type luminaires with High Pressure Sodium lamps to provide maintained (average) illumination levels as follows:

Uniformity

Ratios

Illuminance	(Max/Min.)

A)	Automobile Entrances: 	50 FC		4:1

B)	Drive aisles and Corners:	10 FC		4:1

C)	Between Cars:	  5 FC		4:1

D)	At Walls:	 5 FC		6:1

E)	Upper(roof) Levels	0.6FC       	4:1

F)	Grounds Vehicles and Equipment

parking areas:	2 FC		6:1

G)	Exterior Pedestrian Walkways:  	2 FC		6:1

H)	Stairs:	  15 FC		N/A

Locate parking deck fixtures in linear rows on both sides of the driving lanes. Do not 			locate fixtures directly above driving lanes except where unavoidable at cross aisles.

Coordinate fixture location with parking deck structure.  The maximum distance between 			rows of fixtures parallel to traffic flow is to be 28 feet and the spacing of rows shall be in a uniform grid.

Poured in Place Concrete Structure: Mount fixtures flush to deck using recessed fixture 			boxes.  Center fixtures between structural members.

Precast Concrete Structure: Pendant mount fixtures such that the bottom of the fixture 			aperture is flush with the bottom of precast double tee stems.  Provide bird shroud to prevent nesting and perching and reduce dirt accumulation. Center fixtures between double tee stems.

Other parking structure areas will be illuminated by means of vandal resistant, wet 			location fluorescent lighting fixtures equipped with low temperature ballasts as follows:

A)	Equipment Rooms:	20 FC

Luminaires shall be selected and located so as to minimize glare or light spill over to areas outside the parking structure.

Provide pedestrian walkway lighting outside of the parking structure perimeter using a combination of wall mounted luminaries as indicated in the fixture schedule and pole mounted luminaires to match existing in material, type lamps and spacing.

Provide driveway lighting at exit/entry using pole mounted luminaires to match material and type lamps to that provided for roadway lighting, providing illuminance of 5 FC.

Perform lighting calculations using a maintenance factor of 65%.

All fixtures ballasts shall be high power factor energy savings type.

Provide uninterruptible emergency power to the following portions of the parking structure lighting fixtures to illuminate emergency egress pathways:

A)Parking Areas - 20%

B)Stairways - 50%

Provide illuminated exit signs, connected to uninterruptable emergency power to clearly identify the planned egress paths.

8.5	Lighting Control:

Each level of the parking structure will have separate lighting controls as follows:

A)	Perimeter parking area fixtures B photocell.

B)	Upper Level (roof) lighting poles B photocell.

C)	Stairway, and Elevator Lobbies - unswitched, 24-hour operation.

8.6	Receptacles:

Provide 120V duplex, NEMA 5-20R, GFCI protected receptacles in metal weather and corrosion resistant housing. Locate receptacles at each stairway entry, elevator lobby, equipment rooms, storage room, and near ends of parking ramps.  Provide receptacles at each stair on the second level for vending machines.

8.7	Telephone:

Provide (2) 4@ telecommunications service conduits routed from locations indicated on the drawings to the Electrical Equipment Room. Provide a plywood backboard, grounding bus, termination hardware and duplex receptacle at service conduit entrance.  Owner will provide cable.  Contractor shall pull cable and owner will terminate the cable.

Provide rough in for emergency telephones at each stairtower at each floor on the garage side of the stairtower.  Route one (1) 3/4" empty conduit from each phone location to the electrical room.  Owner will provide phone equipment and wiring.  Provide conduit rough-in for two pay phone locations as specified by the University.

8.9	HVAC Equipment:

Provide branch circuit connections, disconnect switches and motor starters for all mechanical equipment.

8.10	Grounding:

Provide grounding of the electrical system in accordance with the NEC.

8.11	Conduit:

Conduit embedded in concrete, buried or exposed shall be rigid nonmetallic schedule 40 (PVC). Exposed surface mounted conduit shall be installed tight against underside of slabs and tight against walls or columns on surfaces not subject to vehicular impact.

8.12	Electrical Equipment Room:

Provide electric service entry room sized according to codes and standards.  Provide a locking entrance door accessed from the parking/traffic aisle areas with access unrestricted by parking. Provide heating and ventilating as required by code and as indicated herein.

- EVALUATION PROCEDURES

A.	GENERAL INFORMATION/QUALITY/COST POINTS

The purpose of the evaluation process is to establish, through the application of uniform criteria, the quality of each proposal.  The evaluation will be based on the parking structure alone.  Any proposals which have major deviations from the Design/Build Guidelines will be considered non-responsive.  Each proposal will be evaluated by an Evaluation Board appointed by the Owner.

Point values will be assigned up to the maximums for each category in the following table:

Category							Points		Total Points

Quality

1.	Appearance						200

2.	Durability/Maintainability			100

3.	Functionality						150

4.	Safety/Security						50

Total Points For Quality									500

Cost												500

Total Quality & Cost Points									1000

Parking Spaces

Consideration will be given for the number of parking spaces greater or less than 1800. There will be one (1) point subtracted for each space under or one-half (1/2) point added for each space above 1800 spaces.

Points for additional parking spaces will not be considered in evaluating the required minimum 350 quality points for a responsive proposal.

These major areas are further defined in the Technical Evaluation Criteria included in this Section, and will be the basis upon which a total Quality Point Value will be assigned to each proposal.

The Evaluation Board will assign points to each proposal within these major areas by evaluating each element in the Technical Evaluation Criteria, which is keyed by sub-paragraph number to the Program and Design Criteria, Section II of Supplemental Special Conditions.

B.	EVALUATION PROCESS

Each proposal will undergo a two-phase evaluation procedure.

1.	Evaluation Board

The Evaluation Board, selected by the Owner from his staff, and The Owner=s Technical Consultant will prepare a detailed review of each proposal and assign a Quality Point Value to each item indicated in the Technical Evaluation Criteria.

The Board may, in the course of their review, find that some clarification of a proposal is necessary and required for a fair and objective evaluation.  In that event, such clarification will be requested in writing, through the University of Missouri, Project Manager and the proposer given an opportunity to respond in writing.  Proposers are not to assume they will be contacted or afforded an opportunity to clarify or discuss their proposal.

2.	Interview:

Finalists having submitted the proposals which the Owner believes to best meet the requirements of these proposal guidelines may be interviewed by a panel of Owner representatives.  A maximum of five (5) Proposer Representatives shall be permitted at the interview session.  One of the representatives shall be the Proposer=s Project Manager responsible for construction of the proposed structure, one shall be the Prime Professional=s design manager for the project and the remaining three are at the Proposer=s option.

C.	NON-RESPONSIVE PROPOSALS

1.	During the evaluation process it may become apparent that one or more of the proposals do not qualify for consideration on the basis of technical evaluation deficiencies.  If so determined by the Evaluation Board, these proposals will be returned to the Proposer as non-responsive.  Also, any proposal with less than 350 quality points or which exceeds the Design/Build budget will be considered non-responsive.

D.	ESTABLISHMENT OF APPARENT BEST PROPOSAL

After the review of proposals the following equation will be used.

(Lowest Cost Responsive Proposal) x 500  + Quality Point Value " Points for Parking Spaces = Total Points

(Proposer=s Cost Proposal)

The highest combined point total is thus determined and the apparent best proposal announced.

Examples:

Proposal 001 - ($13,400,000) x 500 + 400 + 10 = 906

$13,500,000

Proposal 002 - ($13,400,000) x 500 + 380 + 5 = 881

$13,500,000

Proposal 003 - ($13,400,000) x 500 + 365 + 0 = 865

$13,400,000

Proposal 004 - ($13,400,000) x 500 + 320 + 10 = 845

$13,000,000

Non-responsive/quality points < 350.

Proposal 005 - ($13,400,000) x 500 + 450 + 10 = 952

$13,600,000

Non-responsive/Exceeds budget.

Proposal Number 001 is determined to be the apparent best proposal.  It must be noted that in these examples, the low cost proposal does not represent the highest point proposal submitted.  The highest point total must meet budget and quality point requirements

Total points of the proposal will be done utilizing the format indicated above.  Award of contract will be to the apparent best proposer.

Upon award of contract, the Technical Proposal and other proposal documents submitted by the apparent best proposer will be available for review by all interested participants.  Detailed analysis and technical evaluation data for all other proposals will be retained by the owner in confidence and  will not be available for review.

TECHNICAL EVALUATION CRITERIA

1.	Site Design:

This area of evaluation includes overall planning, layout, design and aesthetic development of the parking facility site and circulation systems.  It embraces considerations of appearance, compatibility of grounds and buildings, relationship to the site and the existing adjacent structures, site access, stacking area for cars entering garage, site distance and ease of merging when exiting garage and other required site considerations as previously indicated.

Generally excluded in this section are considerations of the relative quality of building and landscaping materials.

A.	Site Planning Factors: (70 points)

1)	Maximization of site area.

2)	Open space between parking structure and Virginia Avenue at East Side.

3)	Parking structure vehicular access compliance with program.

4)	Site furnishings compliance with program.

5)	ADA compliance for all on-grade pedestrian entries.

B.	Civil Engineering: (30 points)

1)	Compliance with referenced codes and standards.

2)	Evidence of build ability of utilities within phasing and shutdown parameters.

2.	Parking Structure Design:

A.	Structural Systems and Planning Elements (75 points)

1)	Compliance with program for selected structural system.

2)	Evidence of build ability for structural and foundation systems/assumptions.

3)	Openess of parking areas.

4)	No intrusion of vertical elements into parking stalls.

5)	Compliance with program for clear heights.

6)	Minimization of ramp=s slopes.  Need for electric snow melt cabling.  The use of snow melt cabling will result in negative points.

7)	Sufficient slab drainage.

B.	Visual/Aesthetic Factors: (150 points)

1)	Harmonious exterior materials.

2)	Articulation of the structure through modulation of surfaces.

3)	Articulation of vertical circulations, shear walls and entries.

4)	Design elements used in providing snow dump from upper deck.

5)	Compliance with the program for architectural style of college gothic and the theme of the older  Awhite campus@.

6)	Compliance with master plan build to lines at north and west.

C.	Light/Air Quality/Security Factors (25 points)

1)	Control of headlamp glare from parking structure.

2)	Visibility within parking structure and into stair towers.

3)	No confined or concealed spaces.

4)	Control of light spilling over into adjoining area.

D.	Traffic/Parking Elements: (80 points)

1)	Compliance with the program requirements for circulation.

2)	Clarity of circulation paths with a minimum number of traffic conflict points.

3)	Compliance with the program requirements for parking stall design and accessible parking spaces.

4)	Lack of visual obstructions at ingress/egress points.

5)	Compliance with program requirements for parking controls and graphics/signs.

6)	Consistency to existing MU campus systems.

E.	Vertical Circulation/Shell Office Space: (25 points)

1)	Compliance with the program requirements for passenger elevator and exit stairs.

2)	Openness and visibility of elevator lobby and exit stairs.

3)	Positive slab drainage/curbs away from vertical elements.

4)	Shortest travel distance for traffic to reach next parking level.

5)	Provision of shell space in excess of 14,000 and 7,500 SF.

F.	Mechanical/Plumbing Systems: (10 points)

1)	Compliance with the program requirements for mechanical/plumbing systems.

2)	Routing of internal drains

G.	Electrical Systems: (35 points)

1)	Compliance with the program requirements for electrical systems.

2)	Evidence of compliance with required levels at entrances and the limits of light level variances within the parking structure.

3)	Containment of light within the parking structure.

4)	Efficiency of lighting operations

END OF SUPPLEMENTAL SPECIAL CONDITIONS